## Slide 1
14
0
34
54
165
Ethernet Protocol as Link Layer
IPv4
as Internet Layer
TCP as Transport Layer
HTTP GET as Application Layer/Message
Ethernet Header (14 bytes)
IPv4 Header (20 bytes)
TCP Header (20 bytes)
Application Header + Message (111 bytes)
Frame/Packet (165 bytes)
Layer | Protocol | Position (bytes) | Size (bytes) | Header Size (bytes) | Payload Size (bytes)
(Frame) | - | 0 | 165 | - | -
Link | Ethernet | 0 | 165 | 14 | 151
Internet | IPv4 | 14 | 151 | 20 | 131
Transport | TCP | 34 | 131 | 20 | 111
Application | HTTP | 54 | 111 | - | -

## Slide 2
Version | Header Length
(1 byte)
Differentiated Services Field
(1 byte)
Total Length
(2 bytes)
ID
(2 bytes)
Reserved Bit | Don’t Fragment Bit | More Fragments Bit | Fragment Offset
(2 bytes)
Time to Live
(1 byte)
Protocol
(1 byte)
Header Checksum
(2 bytes)
Source IP Address
(4 bytes)
Destination IP Address
(4 bytes)

## Slide 3
Source Port
(2 bytes)
Destination Port
(2 bytes)
Sequence Number
(4 bytes)
Acknowledgment Number
(4 bytes)
Header Length | Flags
(2 bytes)
Window Size
(2 bytes)
Checksum
(2 bytes)
Urgent Pointer
(2 bytes)
TCP Segment Data
(279 bytes, depends on how much actual data is transmitted)

## Slide 4
Host
My Computer
10.96.200.173
Host
Remote Server
www.google.com
SYN (Seq=0)
SYN, ACK (Seq=0, Ack=1)
ACK (Seq=1, Ack=1)
Data as HTTP GET Request (Seq=1, Ack=1)
0 ms
1.060
1.099
1.389
Round-trip time
1.06 ms

## Slide 5
Host
My Computer
10.96.200.173
Host
Remote Server
www.google.com
FIN, ACK (Seq=262, Ack=11707)
FIN, ACK (Seq=11707, Ack=263)
ACK (Seq=263, Ack=11708)
0 ms
0.810
0.835
Round-trip time
0.81 ms